## Slide 1: FRISBEE DEMO
it is MAGLEV ,not ultimate

## Slide 2: EDDY CURRENT
Eddy current are induced current in shape of loop within conductors due to changing magnetic fields. (Faraday's Law)
The current flows in perpendicular to magnetic field and the concentrates near the surface of conductor. (Depth of Penetration)

## Slide 3: Influencing Factors of Eddy Current
Strength of current changes with:
  The strength of magnetic field proportionally.
  The are of loop proportionally.
  The rate of change flux proportionally.
  The resistivity of material inversely proportional.
Location of eddy current chages with:
  Frequency
  Conductivity
  Permeability

## Slide 4: Funny Links that can be informative
Imagine It - Eddy current science
Copper’s Surprising Reaction to Strong Magnets
Eddy Current Brake Experiment

## Slide 5: Avoding or Using Eddy Current ?
Dark Side of Eddy Current
Eddy current is unwanted at transformers, inductors and electric motors because of power losses.
The power losses are about basically current flow and resistance of conductors. Also, operation frequency changes losses.
(Eddy Current Loss)
For avoiding the loss, ‘Lamination’ is used.
(Core Construction of Power Transformers)

## Slide 6
May the Eddy Current be
with you
There are more applications such as:
-Electromagnetic braking
-Identification of metals
-Attractive effects
-Vibration and position sensing
-Levitation (Repulsive effects).
Electromagnetic Brakes - How they work

## Slide 7: Magnetic Levitation
Induced current by changing magnetic field creates a opposite magnetic fields within conductors.
The magnetic field cretates a induced emf with 90 degree phase.
If conductivity of material is enough large, eddy current from induced emf is out of phase with inductor current because the current phase depends on below formula at basic R-L circuit.(RL_circuit)

## Slide 8: Current and Voltage Waveform( to look phase)

## Slide 9
Thus,the conductors behaves like ‘diamagnetic materials’. Diamagnetic materials are repelled by magnetic field.
This principle is used for some region.
  Eddy Current Non Ferrous Separator
  Maglev Train

## Slide 10: MAGLEV FRISBEE
The frisbee can float on air with the help of magnetic levitation.
The frisbee has a inductor on surface to create a changing magnetic field.
The eddy current is created at conductor below.
Magic: The frisbee is inflight.

## Slide 11: Heating Up
The setup works for 5 minutes because of heating. All power loss from eddy current is converted heat.( Levitation Coil - Induction Heating)
Ke is eddy coefficient and t is thickness of lamination.
As seen, the heat is excited power and frequency.